## Slide 1
Yang Yang, Mohammad Sonji, Adwait Jog
{yangyang, npv2tk, ajog} @virginia.edu
Insight Computer Architecture Lab
Dissecting Performance Overheads of Confidential Computing in GPU-based Systems
ISPASS’25@Ghent
Notes: Hi, my name is Yang Yang.
Today, I will present our work “Dissecting Performance Overheads of Confidential Computing in GPU-based Systems”
This work was performed with my colleague Mohammad Sonji and my advisor Adwait Jog at University of Virginia

## Slide 2
Goal: Dissect the performance overheads of GPU-based confidential computing that can motivate various optimizations to address them.
Problem:
Confidential Computing with GPU is emerging
Existing work lacks detailed performance dissection
Optimization insights remain unclear due to limited characterization
Our results on real hardware show that GPU-based CC comes with:
Data Movement Overhead (up to 19.7×)
Low Encryption Throughput (3.36 GB/s)
Kernel Execution Time (up to 164,030.65× with UVM)
Kernel Launch Overhead (up to 5.31×)
Queueing (1.43× and 2.23× on average)
Fusion, overlapping and quantization
https://github.com/insight-cal-uva/hcc-ispass25-artifact
Executive Summary
ISPASS’25@Ghent
Notes: First, let's have an executive summary.
The problem is confidential Computing with GPU is emerging. But existing work lacks detailed performance dissection
Therefore, optimization insights remain unclear, due to limited characterizations.
Our goal is to dissect the performance overhead of GPU-based confidential computing, that can motivate various optimizations to address them.
We showed on real hardware that GPU based CC came with overhead from
data movement,
encryption,
execution
launch and queueing.
And these observations lead to optimization insights, including fusion, overlapping and quantization.
Our artifact is available at this link.

## Slide 3
Abundant Data and Task-level Parallelism
DL/ML/AI
Graphics
HPC
Crypto
Graphs
Genomics
High Throughput + Energy Efficiency
Graphics Processing Units (GPUs)
3
Credit/Source: AMD, NVIDIA, Wiki
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: In recent years, there is growing need for accelerating applications from different domains. Most popular one is Deep Learning and AI.
GPUs are perfect match for these workloads because they have higher fraction of silicon for computation than CPU.
However, as we process these massive amounts of data, new challenges emerge — particularly in ensuring privacy and security.

## Slide 4: Needs for Security and Privacy
Data is Private
  Client privacy (chat bot, …)
  Regulated (GDPR, PII, …)
Data is Massive
  Outsource compute & data to public cloud Infra.
Can cloud service providers be trusted?
4
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: Some data is inherently private and might be protected by regulations such as GDPR.
The scale of data and
compute demands
quickly exceeds local capabilities.
As a result, users outsource both their data and computation to the cloud to leverage its resources.
But this raises a critical question: <Click> Can we trust cloud service providers?
The answer is no — existing attacks have shown that cloud infrastructures cannot be fully trusted.

## Slide 5: Trusted Computing
ARM
TrustZone
2002
Intel
SGX
2015
AMD
SEV
2016
RISC-V
KeyStone
2019
AMD
SEV-SNP
2020
RISC-V
Penglai
2020
Intel
TDX
2020
ARM
CCA
2021
Intel
SPR
2023
Intel
EMR
2023
CPUs With TDX
NVIDIA
HCC
2023
The first
commercial GPU TEE
VM-based
Isolation
CC
Consortium
2019
Credit/Source: ARM/INTEL/AMD/CCC/RISC-V/NVIDIA/Wiki
5
GPU-based CC
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: To address these trust concerns, both industry and academia have invested heavily in trusted computing or trusted-execution environment (TEE), and more recently this term evolved to confidential computing.
In 2002, ARM proposed TrustZone, which brings hardware-enforced isolations
Intel proposed SGX, which adopts enclave-based isolation and memory encryption
It has been studies for so many years until now
in 2016, AMD proposed SEV shifting the focus toward VM-based isolation.
Since then, most industry solutions have adopted VM-based isolation.
<click> In 2019, the Confidential Computing Consortium was established and many company were involved
Shortly after, we saw new designs like Intel TDX, AMD SEV-SNP, and ARM CCA around 2020–2021, bringing confidential computing to the stage.
In 2023, two major milestones arrived:
<click> Intel shipped the first CPUs with TDX support, and <click> NVIDIA introduced HCC, the first commercial GPU TEE.
Confidential computing has evolved from mobile devices, to CPUs, and now to GPUs.

## Slide 6: Confidential Computing
CPU Package
PCIe
MEE
(TME-MK)
iMC
LLC
AES-NI
Cores
Trust
boundary
Hardware Platform
6
Introduction
Background
Performance Model
Evaluation
Conclusion
MEE: Memory Encryption Engine
Notes: Then let’s introduce the background of CC.
First, the CPU is within the trust boundary.
it can perform memory encryption through a dedicated memory encryption engine (or MEE) resides in memory controller.
CPU cores can also perform AES with specialized instructions.

## Slide 7: Confidential Computing
CPU Package
PCIe
MEE
(TME-MK)
iMC
LLC
AES-NI
Cores
Trust
boundary
Hardware Platform
7
DDR
Introduction
Background
Performance Model
Evaluation
Conclusion
MEE: Memory Encryption Engine
Notes: Then we need to encrypt the DDR memory connected with the CPU through this engine.

## Slide 8: Confidential Computing
CPU Package
PCIe
MEE
(TME-MK)
iMC
LLC
AES-NI
Cores
Trust
boundary
Hardware Platform
8
DDR
TDX Module
Hypervisor
Trust Domain
Isolation
Traditional VM
APP
OS
APP
OS(+TDX)
Introduction
Background
Performance Model
Evaluation
Conclusion
MEE: Memory Encryption Engine
Notes: Now we can launch the virtualization stacks.
We have traditional virtual machine, which is managed by the Hypervisor.
We also have this new type of VM called trust domain which is managed by a trust software component called TDX module.
and there is isolation between different types of VMs.

## Slide 9: Confidential Computing with GPU
PCIe
MEE
(TME-MK)
iMC
LLC
AES-NI
Cores
Trust
boundary
Hardware Platform
9
DDR
TDX Module
Hypervisor
Trust Domain
Isolation
Traditional VM
APP
OS
APP
OS(+TDX)
PCIe
GMMU
Compute
Engines
HBM
Introduction
Background
Performance Model
Evaluation
Conclusion
MEE: Memory Encryption Engine
CPU Package
GPU Package
Notes: Now, we're trying to connect GPU with into this stack.
Once we plugged the GPU, we can set it to confidential computing mode, and passthrough it to the TD

## Slide 10: Confidential Computing with GPU
PCIe
MEE
(TME-MK)
iMC
LLC
AES-NI
Cores
Trust
boundary
Hardware Platform
10
DDR
TDX Module
Hypervisor
Trust Domain
Isolation
Traditional VM
APP
OS
APP +
CUDA
OS(+TDX)
PCIe
GMMU
Compute
Engines
HBM
Introduction
Background
Performance Model
Evaluation
Conclusion
MEE: Memory Encryption Engine
CPU Package
GPU Package
Notes: because of the VM-level isolation, we can install cuda as usual

## Slide 11: Confidential Computing with GPU
PCIe
MEE
(TME-MK)
iMC
LLC
AES-NI
Cores
Trust
boundary
Hardware Platform
11
DDR
TDX Module
Hypervisor
Trust Domain
Isolation
Traditional VM
APP
OS
APP +
CUDA
OS(+TDX)
PCIe
GMMU
Compute
Engines
HBM
Introduction
Background
Performance Model
Evaluation
Conclusion
MEE: Memory Encryption Engine
CPU Package
GPU Package
Notes: the communication over the untrusted PCIe will be encrypted.
because of the lack of dedicated AES engines,
<click> This encryption will go through the CPU cores with the help of AES instructions for acceleration.

## Slide 12: Confidential Computing with GPU
PCIe
MEE
(TME-MK)
iMC
LLC
AES-NI
Cores
Trust
boundary
Hardware Platform
12
DDR
TDX Module
Hypervisor
Trust Domain
Isolation
Traditional VM
APP
OS
APP +
CUDA
OS(+TDX)
PCIe
GMMU
Compute
Engines
HBM
DMA/MMIO
Communication (MMIO/DMA) will trigger #VE, TD will context-switch
Introduction
Background
Performance Model
Evaluation
Conclusion
MEE: Memory Encryption Engine
CPU Package
GPU Package
Notes: whatever happens over the PCIe Bus will be encrypted, which, including the DMA and MMIO operations.
<click> Once GPU received the data, it will be decrypted and stored in HBM.
<click> Such communication with GPU will trigger virtual exception which will cause the context switch from Trust Domain to hypervisor.
Though there have been research to build GPU TEEs, H100 CC is the first commercialized GPU TEE.
Therefore, detailed performance dissection is crucial but not there before.

## Slide 13: Real World Setup
CC-capable CPUs: support TDX or SEV-SNP
H100 is the first GPU that supports CC.
https://github.com/insight-cal-uva/hcc-ispass25-artifact
13
Problem:
Confidential Computing with GPU is emerging
Existing work lacks detailed performance dissection
Optimization insights remain unclear due to limited characterization
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: Guided by the problems,
<click> we set up real hardware to dissect its performance.
The detailed configuration is listed in the table.

## Slide 14: Performance Model
ALLOC
14
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: Now we introduce a simple model to better understand the performance.
We focus on cuda applications in general.
First, you will need to allocate memory on GPU

## Slide 15: Performance Model
H2D
ALLOC
15
H2D: host (CPU) to device (GPU) copy
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: Then you will need to copy the prepared data from host (or CPU) to device (or GPU), this is also referred as the copy-then-execute model

## Slide 16: Performance Model
LAUNCH1
K1
H2D
ALLOC
16
H2D: host (CPU) to device (GPU) copy
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: Now you can launch a kernel with the kernel launch call

## Slide 17: Performance Model
LAUNCH1
LAUNCH2
K1
K2
H2D
ALLOC
Kernel Queueing Time (KQT)
Kernel Launch Overhead (KLO)
Kernel Execution Time (KET)
17
H2D: host (CPU) to device (GPU) copy
Introduction
Background
Performance Model
Evaluation
Conclusion
Launch Queueing Time (LQT)
Notes: Multiple kernels can be launched consecutively.
Launch operation itself takes some time which is referred as kernel launch overhead, or KLO for short
there are queuing times between consecutive launches. Which is called launch queueing time or LQT
Once the launch command finished, kernels are injected to GPU task queues, waiting for scheduling and execution. This waiting time is described as kernel queueing time or KQT
lastly, the kernel will execute, which is referred as kernel execution time, KET for short.
Previous presenters have covered some of the terms, thanks to them, I don’t need clarify more.

## Slide 18: Performance Model
SYNC
18
H2D: host (CPU) to device (GPU) copy
Introduction
Background
Performance Model
Evaluation
Conclusion
LAUNCH1
LAUNCH2
K1
K2
H2D
ALLOC
Kernel Queueing Time (KQT)
Kernel Launch Overhead (KLO)
Kernel Execution Time (KET)
Launch Queueing Time (LQT)
Notes: And now you will need synchronization to wait the GPU finish the task

## Slide 19: Performance Model
D2H
19
D2H: device (GPU) to host (CPU) copy
H2D: host (CPU) to device (GPU) copy
Introduction
Background
Performance Model
Evaluation
Conclusion
SYNC
LAUNCH1
LAUNCH2
K1
K2
H2D
ALLOC
Kernel Queueing Time (KQT)
Kernel Launch Overhead (KLO)
Kernel Execution Time (KET)
Launch Queueing Time (LQT)
Notes: Then you can copy the results from GPU back to CPU.

## Slide 20: Performance Model
FREE
20
D2H: device (GPU) to host (CPU) copy
H2D: host (CPU) to device (GPU) copy
Introduction
Background
Performance Model
Evaluation
Conclusion
D2H
SYNC
LAUNCH1
LAUNCH2
K1
K2
H2D
ALLOC
Kernel Queueing Time (KQT)
Kernel Launch Overhead (KLO)
Kernel Execution Time (KET)
Launch Queueing Time (LQT)
Notes: lastly, you free those memory buffers.

## Slide 21: Performance Model
LAUNCH1
LAUNCH2
K1
K2
H2D
ALLOC
Kernel Queueing Time (KQT)
Launch Queueing Time (LQT)
Kernel Launch Overhead (KLO)
Launch Execution Time (KET)
SYNC
D2H
FREE
P = Tmem + Σ(KLO+LQT) + Σ[(1-βi )(KET+KQT)] + Tother
21
Time on memory copy
D2H: device (GPU) to host (CPU) copy
H2D: host (CPU) to device (GPU) copy
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: Therefore, the first term in this model is related to time spent on memory copy operations.
As we mentioned before, this data movement is over PCIe and will be encrypted under CC

## Slide 22: Performance Model
LAUNCH1
LAUNCH2
K1
K2
H2D
ALLOC
SYNC
D2H
FREE
22
P = Tmem + Σ(KLO+LQT) + Σ[(1-βi )(KET+KQT)] + Tother
D2H: device (GPU) to host (CPU) copy
H2D: host (CPU) to device (GPU) copy
Introduction
Background
Performance Model
Evaluation
Conclusion
Kernel Queueing Time (KQT)
Launch Queueing Time (LQT)
Kernel Launch Overhead (KLO)
Launch Execution Time (KET)
Notes: The next term is the launch related overhead, we sum up all KLO and LQTs

## Slide 23: Performance Model
LAUNCH1
LAUNCH2
K1
K2
H2D
ALLOC
SYNC
D2H
FREE
β1
β2
23
P = Tmem + Σ(KLO+LQT) + Σ[(1-βi )(KET+KQT)] + Tother
D2H: device (GPU) to host (CPU) copy
H2D: host (CPU) to device (GPU) copy
Introduction
Background
Performance Model
Evaluation
Conclusion
Kernel Queueing Time (KQT)
Launch Queueing Time (LQT)
Kernel Launch Overhead (KLO)
Launch Execution Time (KET)
Notes: Then, we take the kernels into consideration.
kernel execution can be overlapped, therefore we assign each kernel an overlapping parameter beta
And then we sum up all kernel queueing time and kernel execution time with respect to the beta

## Slide 24: Performance Model
LAUNCH1
LAUNCH2
K1
K2
H2D
ALLOC
SYNC
D2H
FREE
β1
β2
24
P = Tmem + Σ(KLO+LQT) + Σ[(1-βi )(KET+KQT)] + Tother
D2H: device (GPU) to host (CPU) copy
H2D: host (CPU) to device (GPU) copy
Introduction
Background
Performance Model
Evaluation
Conclusion
Kernel Queueing Time (KQT)
Launch Queueing Time (LQT)
Kernel Launch Overhead (KLO)
Launch Execution Time (KET)
Notes: And lastly, we account the remaining parts in the critical path as term other, like memory allocation, de-allocation, etc.

## Slide 25: Performance Model
25
P = Tmem + Σ(KLO+LQT) + Σ[(1-βi )(KET+KQT)] + Tother
D2H: device (GPU) to host (CPU) copy
H2D: host (CPU) to device (GPU) copy
Introduction
Background
Performance Model
Evaluation
Conclusion
Kernel Queueing Time (KQT)
Launch Queueing Time (LQT)
Kernel Launch Overhead (KLO)
Launch Execution Time (KET)
Notes: With this model, we have an overview of what should be covered to understand the performance implications.

## Slide 26: Performance Model
Focus of this presentation
  Data movement (H2D, D2H, page migration)
  Encryption
  Kernel Execution
  Kernel Launch
  Queuing
26
P = Tmem + Σ(KLO+LQT) + Σ[(1-βi )(KET+KQT)] + Tother
Introduction
Background
Performance Model
Evaluation
Conclusion
Kernel Queueing Time (KQT)
Launch Queueing Time (LQT)
Kernel Launch Overhead (KLO)
Launch Execution Time (KET)
Notes: With this model, we have an overview of what should be covered to understand the performance implications.

## Slide 27: Transfer Bandwidth
Fig.1 Copy bandwidth
Base
Observation 1.
PCIe bandwidth utilization in CC mode drops significantly compared to non-CC.
27
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: Now lets looks at our evaluation.
First, memory copy bandwidth is shown in the figure.
Here we show two types of memory buffers, which is pinned memory and pageable memory
The first observation is PCIe bandwidth utilization in CC mode drops significantly compared to non-CC (also denoted as the base).
Which is shown by the purple arrow.

## Slide 28: Transfer Bandwidth
Fig.1 Copy bandwidth
Base
Observation 1.
PCIe bandwidth utilization in CC mode drops significantly compared to non-CC.
Bandwidth gap between pageable and pinned memory observed in non-CC mode disappears in CC mode, suggesting that pinned memory relies on pageable mechanisms in CC mode.
28
pinned
pageable
Introduction
Background
Performance Model
Evaluation
Conclusion
?
Notes: Then we look at these 2 types of buffer
pinned memory, or pageable memory.
In base case or non-CC case, there is a huge gap between pinned memory and pageable memory which is denoted by the Red Arrow.
But this gap disappeared in CC. Mode, suggesting that pinned memory in CC relies on pageable mechanisms.
And note that the maximum bandwidth CC could reach is 3.03 GB per second. Why its that low?

## Slide 29: Crypto Throughput
Fig.2 Crypto throughput
AES is on the critical path.
Observation 2.
The absence of dedicated hardware AES engines results in low encryption throughput, even when using AES-NI acceleration.
While alternative cryptographic algorithms may offer higher throughput, they often come at the cost of weaker security guarantees.
8.9GB/s
29
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: One main reason to such low bandwidth is the low crypto throughput.
We measured different crypto operations.
Our observation here is the absence of dedicated hardware aes engines, results in low encryption throughput. Even when using the aes instruction for acceleration.
For example, AES-GCM can only reach 3.36GB/s, which is slightly higher than the memory copy bandwidth.
And there are some other alternative cryptographic algorithms, which may offer higher throughput, but they come at the cost of weaker security guarantees.
Because AES is on the critical path, So such overhead comes to the performance directly.

## Slide 30: Kernel Execution Time
Fig.3 Normalized kernel execution time.
Observation 3.
CC has minimal impact on non-UVM kernels (0.48% increase).
30
Non-CC
?
Execution is locked inside GPU, no interaction with CPU
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: Next we look at the kernel execution time.
Here we first show the non-UVM CC kernel execution time, in blue bars. We will talk about UVM or unified virtual memory soon.
we realized that CC has minimal impact on non-uvm kernels. Which is only a 0.48% increase.
Why? Because execution is locked inside the GPU, and when no UVM is used, there is no interaction with the CPU when the computation is going on.

## Slide 31: Kernel Execution Time
Fig.3 Normalized kernel execution time.
31
Non-CC
5.29×
Source: NVIDIA
Single Address Space
Introduction
Background
Performance Model
Evaluation
Conclusion
Frequent CPU-GPU interaction!
Notes: Next we look at the base plus UVM case.
and we saw a 5.2 times increase on average.
This is expected from the UVM mechanisms.
So, what is UVM?
UVM provides you a single address space between CPU and GPU.
and you can trigger page migrations through page fault on GPU or CPU.
However, both page fault handling and migration are expensive.
So, UVM leads to frequent expensive CPU-GPU interactions.

## Slide 32: Kernel Execution Time
Fig.3 Normalized kernel execution time.
32
Non-CC
5.29×
Source: NVIDIA
Single Address Space
ENC/DEC
With CC ON
Introduction
Background
Performance Model
Evaluation
Conclusion
Frequent CPU-GPU interaction!
Notes: Which will be even worse under CC
the page migration will also trigger encryption and decryption transparently.

## Slide 33: Kernel Execution Time
Fig.3 Normalized kernel execution time.
33
Non-CC
164,030.65×
5.29×
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: Then how CC plus UVM looks like.
We quickly observed that it could reach up to 126,000 times increase in execution time.

## Slide 34: Kernel Execution Time
Fig.3 Normalized kernel execution time.
34
Non-CC
164,030.65×
5.29×
188.87×
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: and on average it contributes to a 188 times increase on execution time.

## Slide 35: Kernel Execution Time
Fig.3 Normalized kernel execution time.
Observation 3.
CC has minimal impact on non-UVM kernels (0.48% increase).
UVM in CC mode incurs an average slowdown of 188.87×.
35
Non-CC
164,030.65×
5.29×
188.87×
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: This finished our observation 3.

## Slide 36: Memory Transfer Time
Fig.4 Time (𝜇s) spent on memory copy.
Observation 4.
On average, copy operations in CC mode take 5.80× longer compared to non-CC mode, with a maximum slowdown of 19.69×.
Pinned memory is converted to UVM encrypted paging in CC mode which incurs high overhead.
Pinned memory
36
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: Then we look at memory transfer time.
Our observation here is on average copy operation in CC mode will take 5.8 longer compared to non-CC mode with a maximum slowdown of over 19 times.
as we mentioned before, pinned Memory is converted to UVM encrypted paging in CC, which also incur high overhead.

## Slide 37: Launch and Queuing
5.31×
1.42×
1.43×
2.32×
Fig.5 Effect of CC on KLO, LQT, and KQT.
Results are normalized to non-CC time.
37
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: Now we look at the launch and queueing overhead.
The impression here is CC will increase launch overhead and queueing times.
For example, CC could cause up to 5.3x increase in KLO

## Slide 38: Closer Look
Fig.6 Simplified call stack of a cudaLaunchKernel call, obtained via perf.
Shared memory related
TD VM-Exit related
Observation 5.
On average, CC increases KLO by 1.42× mostly due to TDX hypercalls. It increases LQT by 1.43× and KQT by 2.32×.
For applications with a low number of kernel launches, KQT can be significantly amplified.
38
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: For kernel launch, we can take a closer look
Here we show a simplified call stack of the launch call
<click>
We can observe that in CC, there will be some time spend on setting up shared memory, because this is required for communicating with external device
Which is also required by TDX isolation.
<click>
Then there is also context switch to handling communication via TDX hypercalls
<click>
Therefore, our observation here is
On average, CC increases KLO by 1.4 times mostly due to TDX hypercalls. It increases LQT by 1.4 times and KQT by 2.3 times.
For applications with a low number of kernel launches, KQT can be significantly amplified.

## Slide 39: Case Study
When it starts
How long it takes (duration)
Launch
Kernel
Σ(KLO+LQT)
Σ(KET+KQT)
Fig.7 Distribution of events and their durations for representative applications, in 𝜇s.
Introduction
Background
Performance Model
Evaluation
Conclusion
39
Last Kernel
Notes: Lastly, we put them together, and go through a case study
Here, 2 applications are shown with detailed event timeline
Two type of events are shown, namely Kernel Launch event and kernel execution event
To read this figure
<click>
First, the x-axis stands for when it starts
<click>
And the y-axis stands for how long it last (or the duration)
<click>
here the launch event for both non-CC and CC are shown
And kernel event are shown as well.
and an approximation of the total event duration can be viewed as the distance across the x-axis.
First, you can quickly observe that the CC launch duration increased. And this increase has different impacts to the last kernel finish time.
for application A, the last kernel finish time is not affected by launches.

## Slide 40: Case Study
Fig.7 Distribution of events and their durations for representative applications, in 𝜇s.
When it starts
How long it takes (duration)
Launch
Kernel
Σ(KLO+LQT)
Σ(KET+KQT)
Increased cycles
Last Kernel (Base)
Dominated by Launch
Introduction
Background
Performance Model
Evaluation
Conclusion
40
Last Kernel (CC)
Notes: However, for application B, we observed increased cycles in kernel finish time.
Due to the increased launch duration, the last kernel finish time is actually dominated by its last launch operation.

## Slide 41: Case Study
Fig.7 Distribution of events and their durations for representative applications, in 𝜇s.
When it starts
How long it takes (duration)
Launch
Kernel
Σ(KLO+LQT)
Σ(KET+KQT)
Increased cycles
Dominated by Launch
CC won’t delay the finish of kernels.
CC will delay the finish of kernels.
How to optimize?
Insights: Fusion and overlapping!
Introduction
Background
Performance Model
Evaluation
Conclusion
41
Fusion
Last Kernel (Base)
Last Kernel (CC)
Notes: Therefore we can conclude that for some applications like A
CC won't delay the finish of kernels.
but for some other applications like B.
CC Will delay the finish of kernels.
So how to optimize it?
our insights are, you can use fusion and overlapping.
Next, we briefly discuses the insight of fusion, more details can be found in the paper.

## Slide 42: Insight: Fusion
42
Launch a new kernel
shows high KLO.
First few launch
shows high KLO.
CC-ON
CC-OFF
K1
K2
K1
K2
K1
Introduction
Background
Performance Model
Evaluation
Conclusion
Aggressive fusion is not working, a right fusion parameter helps.
Fuse 128 -> 1
Notes: Here we briefly describe the intuition.
we show kernel launch overhead of a simple 2 kernel scenario, where we launch k1 for 100 time, followed by K2 by 100 time, and we repeat this process.
First, we saw that launch a new kernel, always show a higher kernel launch overhead.
and first few launches to a new kernel shows also higher launch overhead.
With this heuristics, fewer kernel launches, often show extreme high kernel launch overhead
and there should be an optimization space where the number of launches could balance the KLO.
We fuse 128 kernels to one kernel gradually.
And here are the results showing the kernel launch overhead and launch queueing time respectively
We still see that when you do aggressively fusion like to one or 2 kernels, the kernel launch overhead is extremely high.
therefore aggressive fusion is not going to work. A right fusion parameter will help, and we leave this to our future work.

## Slide 43: More Details
Memory Management
Kernel-to-Launch Ratio
Overlapping
CNNs
LLMs
Quantization
…
More details in the paper!
43
Introduction
Background
Performance Model
Evaluation
Conclusion
Notes: And more details including CNNs, LLMs, quantization can be found in the paper. Please check it for more details.

## Slide 44
We present a comprehensive performance evaluation of GPU-based CC guided by a simple performance model, and considered several optimizations towards addressing the overheads of CC.
Our results on real hardware show that GPU-based CC comes with:
Conclusion
Data movement: 5.80× (avg) 19.69× (max) 3.03 GB/s
Encryption: 3.36 GB/s (AES-GCM)
Kernel Execution: 0.48% (CC) 188.87× (avg, CC+UVM)
Kernel Launch: 1.42× (avg) 5.31× (max)
Queuing: 1.43× (avg, LQT) 2.23× (avg, KQT)
Introduction
Background
Performance Model
Evaluation
Conclusion
44
Notes: To summarize,
We present a comprehensive performance evaluation of GPU-based CC guided by a simple performance model, and considered several optimizations towards addressing the overheads of CC.
Our results on real hardware show that GPU-based CC comes with different overhead across different components. The values are shown below.
and with all those information we can have a summary timeline figure showing that
the plain CC, came with encryption and Api of overhead.
When it turns to UVM it came with encrypted paging overhead, which largely slow down the application.
CC on GPU is a new topic recently, many explorations and optimizations are on the way, if you’re interested in it and want to play with it, I am happy to talk more off-line.

## Slide 45: Thank You! Questions?
Yang Yang, Mohammad Sonji, Adwait Jog
{yangyang, npv2tk, ajog} @virginia.edu
Dissecting Performance Overheads of
Confidential Computing in GPU-based Systems
Notes: Questions are welcome.
Thank you.